## Slide 1: A Reverse 230U/226Th Radionuclide Generator for Targeted Alpha Therapy Applications
August 23rd, 2022
LA-UR-18-28992
T.E. Mastren and M.E. Fassbender
Los Alamos National Laboratory, P.O. Box 1663, Los Alamos, NM 87545, USA
18th Workshop on Targetry and Target Chemistry (WTTC 18)

## Slide 2: 230U/226Th: a novel -treatment nuclide pair
Similar to 225Ac/213Bi
Production energies available at university/commercial facilities
Indirect application as 226Th:
Th labeling in development;
28.2 MeV combined α-dose
Direct application as 230U: Leverages rich U coordination chemistry; 34.2 MeV combined dose
Compare to 19.5 (225Ac) and 5.9 MeV doses for 213Bi
Makvandi, M., et al., Alpha-Emitters and Targeted Alpha Therapy in Oncology: from Basic Science to Clinical Investigations. Targeted Oncology, 13(2), pp. 189–203 (2018).
Fassbender, M.E., Guest Edited Collection: Radioisotopes and radiochemistry in health science. Sci Rep, 10(1), 340 (2020).

## Slide 3: Production modes for 230U
Direct:
  231Pa (p,2n) 230U
  232Th (α, 6n) 230U
  232Th (3He,5n) 230U
Indirect:
232Th(p,3n) 230Pa
232Th(d,4n) 230Pa
Cumulative cross sections for
232Th(p,3n)230Pa (17.4 d)*
V. Radchenko, et al., Formation cross-sections and chromatographic separation of protactinium isotopes formed in proton- irradiated thorium metal. Radiochim Acta 104(5), 291-304 (2016).
Ideal indirect production energy range: 50  12 MeV

## Slide 4: Formation and Decay of Precursor 230Pa
232Th(p,3n)230Pa
230Th (7.5E4 a)

## Slide 5: Los Alamos Isotope Production Facility Irradiations of Th Metal Foils
Target stacks Al/Ni/Th; integrated beams ~4.5 µAh
Ni monitor foil (25 µm) for 57Ni/57Co ratio
LANL In-house made Th foil, thickness 0.1 mm, p energy loss ~1.5 MeV
Friend, M.T., et. al., Production of 230Pa by proton irradiation of 232Th at the LANL isotope production facility: Precursor of 230U for targeted alpha therapy, Appl Radiat Isot 156, 108973 (2020).

## Slide 6: Energy Determination for 230Pa production via 57Ni/57Co Activity Ratios
Ax = Activity
σx = Effective Cross Section
λx = Decay Constant
tb = Bombardment Time
T. Mastren, et al., Natural Nickel Foil as a Monitor for Proton Energies Ranging from 15-30 MeV, Nucl Instr Meth Phys Res B 443, 1-4.
Date | Energy (MeV) | 230Pa Yield | % of Theoretical | 230Pa Activity/µAh
Jan 2017 | 19 ± 1 | 32.4 µCi (1.2 MBq) | 88 | 7.3 µCi (270 kBq)
Sept 2017 | 24 ± 1 | 45.9 µCi (1.7 MBq) | 118 | 10.1 µCi (374 kBq)
Jan 2018 | 27 ± 1 | 29.7 µCi (1.1 MBq) | 110 | 6.4 µCi (237 kBq)

## Slide 7: Sulfur-based Ligands for the Separation of Protactinium
DGTA (diglycolthioamide,
LANL In-House):
Extraction resin made in house containing a sulfur variant of TODGA
CL Resin (Triskem):
Extraction resin made by Triskem that contains alkyl phosphine sulfides (R3P=S)

## Slide 8
Equilibrium Distribution Coefficients
T. Mastren, et al., “Separation of protactinium employing sulfur-based extraction chromatographic resins”, Anal Chem, 90(11), 7012-7017.

## Slide 9: Chemical Separation of Pa
Irradiated a 0.1 mm 232Th target with 22.0 MeV protons for 5 µAh
Dissolved target containing 230Pa and fission products in 10 M HCl spiked with HF
Bulk thorium and fission products
4 M HCl/0.1 M HF
230/233Pa and 95Nb
Convert to 10 M HNO3
1 mL CL Resin
50-100 µm mesh
95Nb
1 M HNO3
4 M HCl/0.1 M HF
93 ± 4 % Recovery of Pa
99.8% 230/233Pa
0.2% 95Nb
233Pa is ~7% of total Pa activity
1 mL DGA Resin
50-100 µm mesh
Hopkins, P.D., et al., Synthesis and radiometric evaluation of diglycolamide functionalized mesoporous silica for the chromatographic separation of actinides Th, Pa and U. Dalton Transactions, 47(15), 5189–5195 (2018).

## Slide 10
Direct-Phase Concept: 230Pa/230U Separation
CL
Column
230Pa in 10 M HCl
5mL 10M HCl
Elute >95% of the 230U with >99.99 % purity
for direct use or use in 226Th generator
Binds 230Pa
T. Mastren, et al., A Reverse 230U/226Th Radionuclide Generator for Targeted Alpha Therapy Applications, Nucl Med Biol 2020, 90-91, 69–73.

## Slide 11: Reverse-Phase Generator: 230U/226Th Separation
230U/226Th in equilibrium
Column
<0.001% 230U/226Th
5mL 0.1M HNO3
Elute 230U
(>99.8 %)
1mL 0.1M Citrate, pH 5
Elute ~96% 226Th (<0.18% 230U)
Wash Column w/ 10mL water
Add 6mL Concentrated HCl to 230U Fraction
Equilibrate Resin with 2mL conc HCl
Binds 230U/226Th
100 μg DGA Resin
Successful chelation studies with 70 µCi of 230U/226Th
Two more generator concepts in development (230U sorption/ 226Th elution)
Ferrier, M.G., et al., Thorium chelators for targeted alpha therapy: Rapid chelation of thorium-226. J Labelled Comp. Radiopharm. 63(12), 502–516, (2020).

## Slide 12: 230U/226Th Generator Elution Evaluation (6 weeks)
Chart: pH Dependence of Elution
| 2 | 3 | 4 | 5
 | 92 | 95.7663 | 95.1567 | 97.3198
1
2

## Slide 13: Conclusions
Separation of 230Pa from bulk thorium targets and co-produced fission products
Designed a dual generator system first to yield 230U from 230Pa and second to yield 226Th from 230U
Generator provides 226Th in a chelated form, which is amenable to direct labeling due to short 30.6 minute half-life
Precedence for optimized Th chelates with fast complexation kinetics
Follow-on work granted for FY20(larger scale production of 230U, Th chelator development, call FOA-LAB-18-1896)

## Slide 14: Acknowledgment
This research was supported by the U.S. Department of Energy Isotope Program, managed by the Office of Science for Isotope R&D and Production
(Grants FOA LAB 14-1099 and LAB 18-1896)