## Slide 1
Towards optimized production of 155Tb with solid targets
at the Bern medical cyclotron
G. Dellepiane1, P. Casolaro1, C. Favaretto2, P.V. Grundler2, I. Mateu1, P. Scampoli1,3, Z. Talip2, N.P. van der Meulen2, S. Braccini1
1 Albert Einstein Center for Fundamental Physics, Laboratory for High Energy Physics, University of Bern, Switzerland
2 Center for Radiopharmaceutical Sciences, Paul Scherrer Institute, Villigen, Switzerland
3 Department of Physics «Ettore Pancini», University of Napoli Federico II, Complesso Universitario di Monte S. Angelo, Italy

## Slide 2
G. Dellepiane – WTTC18
clustered DNA damage
DNA
Charged particle track
α, β-, Auger emitter
Targeted radionuclide therapy (α, β-, Auger)
Theranostics in nuclear medicine
PET / SPECT imaging
(β+ / γ)
β+ emitter
Positron
Electron
511 keV gamma ray
511 keV gamma ray
γ emitter
gamma ray
Research program ongoing at the Bern cyclotron laboratory:
Theranostic and non-standard radioisotope production with solid targets;
Accelerator and detector physics developments;
Proton beam energy measurement;
Nuclear cross-section measurements.
Terbium: the Swiss Army Knife
Tb 149
4.1 h
ε
α β+
γ
Müller et al. 2012 J Nucl Med 53 1951
Tb 152
17.5 h
ε β+
γ
β-
γ
e-
Tb 161
6.90 d
ε
γ
Tb 155
5.32 d
SPECT
PET
Auger-therapy
α-therapy

## Slide 3
G. Dellepiane – WTTC18
The Bern medical cyclotron laboratory
IBA 18/18 HC cyclotron
Two H- ion sources
High current (max 150 µA)
8 out ports:
  6 18F liquid targets [industrial production]
  Solid Target Station (STS) [research]
  Beam Transfer Line (BTL) [research]
18 MeV Bern medical cyclotron
Beam Transfer Line (BTL)
Solid Target Station (STS)

## Slide 4
G. Dellepiane – WTTC18
Terbium radioisotopes
 | 152Gd | 154Gd | 155Gd | 156Gd | 157Gd | 158Gd | 159Gd
Nat [%] | 0.20 | 2.18 | 14.80 | 20.47 | 15.65 | 24.84 | 21.86
Enr-155 [%] | <0.02 | 0.5 | 91.90(30) | 5.87 | 0.81 | 0.65 | 0.27
Enr-156 [%] | <0.01 | 0.05 | 0.87 | 93.30(10) | 4.38 | 1.08 | 0.32
G. Dellepiane et al, Appl. Radiat. Isot. 2022, 184, 110175
153Tb (t1/2 = 2.34 d)
155Tb (t1/2 = 5.32 d)
154Tb
154gTb
(t1/2 = 21.5 h)
154m1Tb
(t1/2 = 9.4 h)
154m2Tb
(t1/2 = 22.7 h)
ec, β+
78.2%
IT
21.8%
154gTb
154Gd
ec, β+
98.2%
IT
1.8%
154gTb
154Gd
154Gd
ec, β+
100%
154Gd
ec, β+
100%
154Gd
ec, β+
100%
156Tb
156gTb
(t1/2 = 5.35 d)
156m1Tb
(t1/2 = 24.4 h)
156m2Tb
(t1/2 = 5.3 h)
IT
100%
156gTb
IT
100%
156gTb
156Gd
ec, β+
100%
156Gd
ec, β+
100%
156Gd
ec, β+
100%

## Slide 5
G. Dellepiane – WTTC18
Cross-section measurements
Target for cross section measurement: (a) empty aluminum disc (24 mm diameter, 2 mm thick); (b) aluminum disc filled with Gd2O3; (c) aluminum disc covered with a thin aluminum foil
p
Grounded collimator
Electron suppressor ring
Target position
Attenuators position
Aluminum attenuators
Beam current signal
Bias voltage
p
TARGET
COLLIMATOR
UniBEaM detector
Developed by LHEP
commercialized by
D-Pace
Flat beam procedure
Flat proton beam
Attenuators
Collimator
const const
Target material
T.S. Carzaniga et al, Appl. Radiat. Isot. 2017, 129, 96

## Slide 6
G. Dellepiane – WTTC18
Cross-section measurements: 156Tb
156gTb:
156m1Tb:
156m2Tb:
Bateman equations
Gd(p,X)
156gTb
(= 5.35 d)
156m1Tb
(= 24.4 h)
156m2Tb
(t1/2 = 5.3 h)
156gTb
156gTb
IT (100%)
IT (100%)
156Gd
EC, β+ (100%)
156Gd
EC, β+ (100%)
156Gd
EC, β+ (100%)
Method 1: t >> T1/2 (156m1Tb, 156m2Tb)
Fit2 parameters | Fit1 parameters | 
a2 [kBq] | b2 [kBq] | c2 [kBq]
0.726 ± 0.007 | No Signal | 11.6 ± 0.2
cumulative-type 156Tb cross section
Method 2: several measurements during the decay time
Fit1 parameters | 
b1 [E-6 s-1] | (156Tb) [E-6 s-1]
1.53 ± 0.01 | 1.50 ± 0.03
Fit1 parameters | 
b1 [E-6 s-1] | 
1.53 ± 0.01 | 1.50 ± 0.03
Enriched 155Gd2O3

## Slide 7
G. Dellepiane – WTTC18
Cross-section measurements: 156Tb

## Slide 8
G. Dellepiane – WTTC18
Cross-section measurements: 155Tb
Gd(p,X)
155Tb
(= 5.32 d)
155Gd
EC (100%)

## Slide 9
G. Dellepiane – WTTC18
155Tb production
Targets for 155Tb production tests: (a) coin with a 0.24 mm covering lid, containing a ~40 mg 155Gd2O3 pellet; (b) coin with a 7 mm hole in the lid, containing a ~40 mg 156Gd2O3 pellet
Enriched 155Gd2O3
Enriched 156Gd2O3

## Slide 10
G. Dellepiane – WTTC18
155Tb production
Enriched 155Gd2O3
Enriched 156Gd2O3

## Slide 11
G. Dellepiane – WTTC18
Results
C. Favaretto et al, ENJMMI Radiopharm. Chem. 2021, 6, 37
G. Dellepiane et al, Appl. Radiat. Isot. 2022, 184, 110175
 | 155Gd2O3 | 156Gd2O3
Ein [MeV] | 10.5 ± 0.4 | 18.2 ± 0.4
m [mg] | 37.0 ± 0.5 | 37.5 ± 0.5
Q [10-3 µAh] | 5.3 ± 0.3 | 2.6 ± 0.1
Production yield [MBq/µAh] |  | 
155Tb | 3.4 ± 0.2 (3.1) | 11.0 ± 0.6 (12.4)
156Tb - tot | 0.23 ± 0.01 (0.22) | 1.3 ± 0.1 (1.3)
156gTb | 0.14 ± 0.01 (0.16) | 0.93 ± 0.05 (0.91)
156m1Tb | No Signal (0) | 0.32 ± 0.12 (0.34)
156m2Tb | 2.2 ± 0.1 (2.6) | 9.7 ± 0.6 (10.5)
Purity 155Tb |  | 
EoB | 53.3 ± 0.5 (53) | 46.4 ± 0.9 (49)
96 h | 93.4 ± 0.1 (93) | 87.9 ± 0.3 (89)

## Slide 12
G. Dellepiane – WTTC18
Conclusions and outlook
The production of 155Tb was investigated via the 155Gd(p,n)155Tb and 156Gd(p,2n)155Tb nuclear reactions;
Cross sections were measured by irradiating natural Gd, enriched 155Gd and enriched 156Gd targets. No cross-section data were reported for 156m1Tb and 156m2Tb;
The production yield and purity were studied to determine the optimum irradiation conditions;
The 156Gd(p,2n)155Tb route requires a higher beam energy;
Tests were carried out by irradiating enriched 155Gd2O3 and 156Gd2O3 solid targets;

## Slide 13
G. Dellepiane – WTTC18
Conclusions and outlook
The 156Gd(p,2n)155Tb reaction provides a higher yield than the 155Gd(p,n)155Tb but lower EoB radionuclidic purity;
The radionuclidic purity increases over time. 156Tb is the only impurity in the samples;
Off-line mass separation technique to isolate 155Tb;
Further studies to establish the impact of 156Tb from a dosimetry perspective;
The obtained results contribute to pave the way towards the use of medical cyclotrons to produce 155Tb for theranostics.

## Slide 14
G. Dellepiane – WTTC18
Acknowledgments
LHEP engineering and techincal staff
SWAN Isotopen AG maintenance team
Group on radionuclide development at PSI
Group on medical application of particle physics at LHEP

## Slide 15
Thank you all for your attention!

## Slide 16
G. Dellepiane – WTTC18
Cross-section measurements: 156Tb (1)
Gd(p,X)
156gTb
(= 5.35 d)
156m1Tb
(= 24.4 h)
156m2Tb
(t1/2 = 5.3 h)
156gTb
156gTb
IT (100%)
IT (100%)
156Gd
EC, β+ (100%)
156Gd
EC, β+ (100%)
156Gd
EC, β+ (100%)
Fit2 parameters | Fit1 parameters | 
a2 [kBq] | b2 [kBq] | c2 [kBq]
2.45 ± 0.02 | 0.71 ± 0.24 | 22.75 ± 0.87
Fit1 parameters | 
b1 [E-6 s-1] | (156Tb) [E-6 s-1]
1.43 ± 0.10 | 1.50 ± 0.03
Fit1 parameters | 
b1 [E-6 s-1] | 
1.43 ± 0.10 | 1.50 ± 0.03
Enriched 156Gd2O3

## Slide 17
G. Dellepiane – WTTC18
Cross-section measurements: 154Tb
Fit parameters | 
b [E-6 s-1] | (154Tb) [E-6 s-1]
8.98 ± 0.27 | 8.96 ± 0.17
Fit parameters | 
b [E-6 s-1] | 
8.98 ± 0.27 | 8.96 ± 0.17
154Gd
EC, β+ (100%)
Gd(p,X)
154gTb
(= 21.5 h)
154m1Tb
(= 9.4 h)
154Gd
EC, β+ (100%)
ec, β+
78.2%
IT
21.8%
154gTb
154Gd
154m2Tb
(t1/2 = 22.7 h)
154gTb
154Gd
ec, β+
98.2%
IT
1.8%
154Gd
EC, β+ (100%)

## Slide 18
G. Dellepiane – WTTC18
Cross-section measurements: 154Tb