## Slide 1: Crab Cavity Cryomodules for HiLumi
Thomas Jones on behalf of the UK-CERN Team
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 2: Crab Cavities at CERN
LHC Point 1 (horizontal)
2 cavities / IP side/ beam to be installed during LS3
=
4 RFD CM to be installed + 1 CM spare
LHC Point 5 (vertical)
2 cavities / IP side/ beam to be installed during LS3
=
4 DQW CM to be installed + 1 CM spare
SPS BA6
Test Prototype Modules with proton beam
1 DQW proto CM + 1 RFD proto CM
SM18 Area
Cavity cold testing, clean room facilities & cryomodule qualification
Double Quarter Wave (DQW) Cavity (BNL)
RF Dipole (RFD) Cavity (ODU)
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 3: Crab Cavity Cryomodule in LHC Tunnel
LHC integration– courtesy of Maria Gonzalez de la Aleja – ATS/DO
3.4m
0.9m

## Slide 4: RFD Pre-Series Crab Cavity Cryomodule
Fundamental Power Coupler
Frequency Scanning Interferometry
Sector Valve
Thermal Shield
Cryogenic Safety System
Crab Cavity (RFD)
Outer Magnetic Shield
Cold Magnetic Shield (internal)
Cavity Support System
Vacuum Diagnostics
Cavity Tuner
Outer Vacuum Chamber
Cryoline Jumper
Plug in module
CAD Images courtesy of Teddy Capelli CERN/EN-MME

## Slide 5: Beam section of RFD Cryomodule
Extremity vacuum chamber LHCVMACAA_T0001
Extremity vacuum chamber
Extremity vacuum chamber
Extremity vacuum chamber
Beam screen Cold/Warm transition Long
Cavity Cold/Warm transition Long
Inter beam screen plug-in module
Inter cavities plug-in module
Beam screen Cold/Warm transition Short
Cavity Cold/Warm transition Short
Beam screen
Beam screen
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 6: Dressed Crab Cavity
H-HOMs
V-HOMs
Antenna
Cold shield design and production in UK
Helium Vessel Welding at CERN.
Ancillary design and manufacture from CERN

## Slide 7: Outer Vacuum Vessel
RFD outer vessel :
Large gaskets removed for LHC compatibility
Overall dimensions : 2800x950x1300
Mass : 3100kg
St. Steel welded assembly
Brackets take the Top Plate mechanical loads
Image courtesy J.Sauza Bedolla - Lancaster

## Slide 8: Warm Magnetic Shield
  DQW design adapted to RFD
  Forms a “Second Skin” to the Outer Vacuum Chamber
  Material : MuMetal Th.:2mm
  Currently in production in the UK
Mu Metal Spring finger contacts
Shield test setup
Shield supplier production drawings approved

## Slide 9: Thermal screen
Design changes from DQW:
  Copper changed to 3mm thick 6061 T6 Aluminium Alloy plates
  Significant cost and weight saving
  Stainless Steel 316L Cooling circuit
  Adjustable flexure support system
~100 kg
Cooling circuit connection
Support Flexure
11th HL-LHC Collaboration Meeting, Oct ‘21, CERN

## Slide 10: Touch Screen Installed in Design Office
Collaborative procedure development, design review and drawing checks whilst socially distant
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 11: Logistics planning
Development of travellers including outgoing and incoming inspection procedures for all equipment
Using Assembly Building 3D model in planning assembly and storage.
Considerable amount of work to ensure a trouble free transport of goods from CERN to the UK post Brexit.
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 12: RFD2 Cavity and Ancillaries arrived at Daresbury
Arrived 29th September 2021. Careful prior planning led to a trouble free transport
RF Acceptance Testing of the Cavity taking place now
Next Cavity to be delivered early November 2021.

## Slide 13: Pre-Cleanroom Assembly Procedure
Pre-Cleanroom Assembly Procedure Approved
Cleanroom Assembly Procedure - made good progress.
Tooling for first steps is on site.

## Slide 14: Cavity String assembly Lifter
Movement qualified with the laser tracker
<1mm lateral movement over the full stroke
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 15: Transport Frame and Drop Test Kit all on site
Practise assembly of the transport frame
Testing taking place over the next couple of weeks
Lifting gantry
Quick-release hook
Steel plate
1KHz displacement sensors
Wire Rope Isolators

## Slide 16: DQW Pre-Series in industry (@ RI)
DQW Pre-series 1 HPR Preparation
DQW Pre-series 2 Metrology
Cold Test @CERN
Pre-series bare cavity 1:
  Metrology done.
  HPR and Ready for re-CT, week 43/44.
Pre-series bare cavity 2:
  CT successful.
  Currently in metrology.
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 17: DQW Series Cold Magnetic Shield
DQW Production Cold Magnetic Shield
First hardware delivered for HL-LHC-UK Phase 2
Designed by STFC/Lancaster Uni.
Manufactured in UK Industry.
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 18: DQW Series Cryomodule
Design work in progress.
Aim to be as similar to the RFD Pre-series as possible.
Conceptual review in March 2022 at the latest.
Fundamental Power Coupler
Sector Valves
Crab Cavity (DQW)
Cold Magnetic Shield (internal)
Cavity Tuner
Outer Vacuum Chamber
Cryoline Jumper
Plug in module

## Slide 19: Timeline for Crab Cryomodule Production in UK
RFD CM Assembly
30/09/2021 to 08/09/2022
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 20: Conclusions
RFD Pre-Series CM assembly will start in the coming weeks
On track with long lead time procurement/manufacture.
New infrastructure installed at DL for CM assembly.
Testing to take place for the CM Transport Frame
RFD Pre-Series CM assembly should be complete in September 2022
Work started to adapt Cryomodule design for DQW Series.
Series CM assembly to start at DL in January 2023, with 4 modules complete by September 2024.
TRIUMF 2021 EIC Accelerator Partnership Workshop, 27th October 2021

## Slide 21
Any Questions?