## Slide 1: International Collaborations for HL-LHC (Crab Cavities)
HL-LHC WP4, CERN
27 October 2021

## Slide 2: HL-LHC Crab Cavities (WP4)
4+1 RF Dipole cryomodules
US-AUP, Canada, CERN & Russia
4+1 DQW Cryomodules
UK, CERN, Russia
SPS BA6 – CERN & UK
2 Test Prototype
(1-DQW, 1-RFD)
*each cryomodule consists 2-cavities & independent powering system and control /cavity

## Slide 3: Reminder: Dressed Cavity Geometries
/cavity*
()
Common FPC = 40 kW-CW
Operating Temp = 2 K
Double Quarter Wave
RF Dipole
*Engineering spec: 4.1 MV dressed for 20% margin

## Slide 4: 2018: DQW Prototype Module Validated!
Phys. Rev. Accel. Beams 24, 062001
*CERN built with contributions from UK, US & Japan

## Slide 5: RF Dipole Prototype for SPS Tests (CERN + UK)
Dressed cavities CERN
Cryostating at the UK

## Slide 6: RF Dipole Dressed Cavity - CERN
Note: RFD1 tested at 2.5K due to superfluid leak, the leaky flange was tightened at warm
Standardized feedthrough for all HOM couplers validated

## Slide 7: Final Assembly & Transport
RFD2 beam screen assembly
Transport Frame/box
RFD Power couplers
Plug-in-module assembly
Cavity line
Important learning experience both for CERN and collaborations for the series production
(see Wed WP4 parallel)

## Slide 8: RF Dipole 2 Transport (27-Sept, 2021)
CERN-SM18
UK
Dedicated and fully instrumented transport, executed smoothly
See Thursday afternoon session

## Slide 9: Next Steps: RF Dipole Cryostating
Dressed
Cavity
String Assembly
Cryostating
Q3 2022
See next talk: T. Jones
Vacuum vessel leak check
Cryomodule Lifter

## Slide 10: Masterplan of WP4
Courtesy: Planning Team
Prototype (SPS-tests)
HL-LHC Series

## Slide 11: HL-LHC Series (CERN, Canada, Russia, UK, US-AUP)
Components (FPC, beam screen, RF lines, …)
Components
5 DQW cryomodules | 5 RFD cryomodules | 20 Solid State RF Systems
Cavities + processing + helium vessels by Research Instruments (DE) & CERN Cold magnetic shields by UK HOM couplers + antennas by CERN 4 CM by UK (STFC) & 1 CM at CERN with some components from CERN All cavities & CM cold validation tests at CERN (and a few at Uppsala-Sweden) | Bare cavities by Zanon (IT) under US-AUP Processing + cold magnetic shield + helium vessel + HOM couplers + antennas + cold tests by US-AUP 5 CM by TRIUMF-Canada with some components by CERN CM cold validation tests at CERN | High power solid state amplifiers by BINP-Russia High power RF lines, circulators, loads by MEPHI-Russia
HPRF Lines

## Slide 12: Supply Chain Crab Cavities
DQW
RFD

## Slide 13: CERN DQW-Series with Industry
Successful manufacturing of 2 pre-series cavities with industry (RI) with 1-cavity reaching excellent results. Need to improve surface chemistry & cleanliness of the RF surface
Relatively long delays related primarily to conform with eng. specifications and aggravated due to COVID – but now on track for the series phase
DQW-RI

## Slide 14: RFD Series (US-AUP & Canada)
Successful prototyping with industry (Zanon) to finish 2 cavities & test them beyond specification
Significant progress to launch pre-series & series
Preparations at TRIUMF for acceptance tests of dressed cavities
RFD1-AUP
RFD2-AUP
TRIUMF update to test dressed cavities at 2K
Vertical test stand FNAL

## Slide 15: High Power RF for SPS Tests
Two 80 kW IOTs operational in SPS
  Same system already in use for several years in the SPS for 800 MHz harmonic cavities. Adapted at CERN for 400 MHz for crabs
  Rotatable high power waveguides to adapt the table movement
  RF circulators and loads are of LHC type and a bit oversized
Surface installation
~150 m

## Slide 16: Series: High Power RF System & Chain
In-kind contribution BINP-Russia for high power amplifiers (solid state to replace IOT baseline)
In kind contribution for high power RF chain (transmission lines, circulators, RF loads)
UA Gallery on 1-IP side, Amplifiers
HL-LHC Tunnel
UA Gallery to Tunnel Connection
Graphics: Courtesy Integration

## Slide 17: Final Comments
Two cryomodules (DQW & RFD) for SPS tests
  DQW module successfully built at CERN and validated wit beam
  RFD cavities fully validated, being transported to UK for cryostating
  The RFD module is expected to be tested in SPS in 2023
Series production
  Multi-lab collaboration & industry for series production
  Only DQW cavities, HOM couplers, FPCs and some critical components are managed by CERN
  Important contributions from Russia on solid-state power amplifiers and RF power chain for crab cavity powering

## Slide 18: Thanks to HL-LHC management, CERN-Depts and our collaborations for their strong support
Special thanks to all WP4 colleagues for a fantastic job in 2021

## Slide 19: 2021: DQW-SPS Re-commissioning
Important cryogenic consolidation and tuner consolidation completed during LS2. Cavity alignment reproducible ()
Analysis underway WP2/WP4
MD on emittance growth successfully performed 13-Oct-2021 (200 GeV)
X-axis Not fully calibrated
Cavities recommissioned; RF conditioning close to 2 MV. LLRF commissioned to ~1.5 MV
Re-learning of the cavity setup not trivial, also long
(270 GeV)
(200 GeV)

## Slide 20: Cavity Testing at Uppsala/FREIA
USLARP prototype cavity test comparison between SM18 & FREIA – 2020 – successful with slightly lower performance
In 2021, cavity was re-rinsed at CERN for a 2nd validation test
During transport, the vertical test field antenna (fragile connection) fell off and had to sent back to CERN
2020 tests
2021 Antenna issue