## Slide 1: Wire corrector system for the HL-LHC – P530
Marco Marchetto
Group leader Accelerator Engineering Physics
TRIUMF accelerator division
P530 project leader
TRIUMF & ATLAS Canada seminar - September 21st , 2021

## Slide 2: Outline
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Introduction
  terminology
Wire corrector
  concept
  first proof of concept
  numerical calculations
Wire corrector system (P530)
  components
  prototype
TRIUMF expertise
  beam dynamics
  engineering
Summary

## Slide 3: Outline
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Introduction
  terminology
Wire corrector
  concept
  first proof of concept
  numerical calculations
Wire corrector system (P530)
  components
  prototype
TRIUMF expertise
  beam dynamics
  engineering
Summary

## Slide 4: Preamble (acknowledgements)
Most of the material presented here is provided by the CERN collaborators:
Adriana Rossi
Alessandro Bertarelli
Guido Sterbini
Yannis Papaphilippou
Stephane Fartoukh
Nikos Karastathis
Kyriacos Skoufaris
Axel Poyet
TRIUMF & ATLAS Canada seminar - September 21st , 2021

## Slide 5: a CERN initiative…
1997
V. Shilsev et al.
e- Q-compression
2000
J.-P. Koutchouk
DC wires for LHC
March 2017
2nd Workshop on (HL-)LHC
Wire Compensation
2015
S. Fartoukh et al.
PRST-AB 18, 121001
2008
U. Dorda
PhD Thesis
2012
T. Rijoff
M.Sc.Thesis
1999
Y. Papaphilippou, F. Zimmermann
PRST-AB 2, 104001
2004
B. Erdeley, T. Sen
FERMILAB-TM-2268-AD
2007
H. J. Kim, T. Sen
PAC07-THPAN114
2016
A.S. Patapenka et al.
NAPAC2016-TUPOB17
Experiment in the LHC
2017-2018
J.-P. Koutchouk et al.
Wires in the SPS
Since 2004
W. Fischer et al.
Wires in RHIC
2006
C. Milardi et al,
Wires in DAFNE
Since 2006
F. Zimmermann et al.
Specification of the
LHC wires, 2013
1st Workshop on (HL-)LHC
Wire Compensation
December 2015
DC wire proposed for LHC by J.P. Koutchouk in 2000
Experimental tests of DC wires in SPS, RHIC and DAFNE. Long range compensation never demonstrated in hadron collider with operational configurations hence the need for direct experiments in LHC
TRIUMF & ATLAS Canada seminar - September 21st , 2021

## Slide 6: IR & IP
TRIUMF & ATLAS Canada seminar - September 21st , 2021
IR: Insertion Regions located in the straight sections between arcs
  LHC has 8 IR
IP: interaction points where the two counter-rotating proton beams collide
  IP are “special IR”
  LHC has 4 IP (experiments): ATLAS, ALICE, CMS and LHCb
  ATLAS and CMS are referred to as high luminosity experiments
from A. Poyet thesis

## Slide 7: BBLR
TRIUMF & ATLAS Canada seminar - September 21st , 2021
BBLR (Beam-Beam Long Range) are electro-magnetic interactions between the two beams
“BBLR interactions occur around the IP where the two beams come closer to each other”
The closer the beams the stronger the BBLR
“The non-linear part of these long-range interactions appears to be the dominant mechanism for beam blow-up and beam losses”
BBLR needs to be compensated (can not be avoided) to increase beams lifetime

## Slide 8: Luminosity
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Luminosity: proportionality factor between the event rate and the cross-section of the event
measure in cm-2∙s-1
Typically it is quoted the integrated luminosity (rather than previous “peak” luminosity)
measured in fb-1
Luminosity of Gaussian bunches colliding with a crossing angle qc
formulas from A. Poyet thesis

## Slide 9: Crossing angle
TRIUMF & ATLAS Canada seminar - September 21st , 2021
B2
B1
qc (mrad)
Beam separation
(in unit of s, beam size)
Reducing the separation, decrease the crossing (increasing the luminosity) but increase the BBLR
Increasing the separation (to reduce BBLR), increases the crossing angle but reduces the luminosity
from A. Poyet thesis

## Slide 10: LHC vs HL-LHC parameters
TRIUMF & ATLAS Canada seminar - September 21st , 2021
from A. Poyet thesis
from A. Poyet thesis
Because of higher beam intensity (to reach higher peak luminosity) the beam separation had to be increase to reduce BBLR
Increase in crossing angle is compensated by means of the crab cavities (HL-LHC baseline configuration), but
  Only half of the cavities (16) necessary to fully compensate the crossing angle are going to be installed
  Hence beam separation had to be reduced (from 12.5 s to 10.5 s)
LHC integrated luminosity: 60 fb-1
HL-LHC integrated luminosity goal: 250 fb-1
Still integrated luminosity can be augmented even for the baseline by reducing the BBLR

## Slide 11: Dynamic aperture
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Dynamic aperture (DA): “average distance in phase space of the border of stability”
“The numerical estimate of the dynamic aperture is related to the computation of the volume in phase space of the initial conditions that are stable after a give number of revolutions around the machine”
Stability domain: “the region of phase space where one can safely operate the machine”
Short-term stability: 1000 turns (CPU limited)
Dynamic aperture reported in unit of s (beam size)

## Slide 12: Outline
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Introduction
  terminology
Wire corrector
  concept
  first proof of concept
  numerical calculations
Wire corrector system (P530)
  components
  prototype
TRIUMF expertise
  beam dynamics
  engineering
Summary

## Slide 13: The wire compensation concept
TRIUMF & ATLAS Canada seminar - September 21st , 2021
The electromagnetic kick of the long-range beam-beam effect is similar to the one given by a DC wire
Analogy of the wire field with standard multipole magnets  Resonant Driving Terms compensation [S. Fartoukh et al., PRST-AB 18, 121001]
IP
BBLR

## Slide 14: Wire locations
TRIUMF & ATLAS Canada seminar - September 21st , 2021
from A. Poyet thesis
Schematic from J. P. Koutchouk paper
Wires to be located on both side of the interaction point to compensate before and after the IP
First proof of principle accomplished using wire embedded in collimator at IP1 (ATLAS) and IP5 (CMS) for a single beam correction

## Slide 15: Wire-in-collimator demonstrator
TRIUMF & ATLAS Canada seminar - September 21st , 2021
LHC DC wire demonstrators embedded in the jaw of operational tertiary collimators
1-m long Cu wire of 2.48 mm diameter capable to carry up to 350 A
Maximum Current IW=350 A  ~260 ºC
≈1 m
3 mm
2.48 mm
Vacuum tank
Jaws
Actuation system

## Slide 16: Objectives of the experiment
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Prove a beneficial effect of the wire demonstrators in a regime dominated by long-range beam-beam effect. The compensation should not degrade the lifetime of the head-on bunches
Need to guarantee the beam-wire alignment, and that the linear effects of the wire (orbit and tunes) are compensated
The main observables are the beam losses, its lifetime and the bunch effective cross-section (seff)
Intensity loss-rate
Instantaneous luminosity

## Slide 17: Experiment results
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Almost full compensation, even at reduced crossing angle, for regular bunch whereas PACMAN bunch (which experiences fewer long range interactions) are not degraded
~80 mb
Wire alignment
COMPENSATION ON
Current scan example
Transverse blow-up and BBLR signature
COMPENSATION OFF
COMPENSATION ON
Reduction of crossing angle

## Slide 18: Dynamic aperture calculations
TRIUMF & ATLAS Canada seminar - September 21st , 2021
DA calculations shows that BBLR correction allows to:
  run with a smaller crossing angle for the same dynamic aperture (5 s)
  reduce beam losses (because of the bigger dynamic aperture) and therefore reduce background noises
  reduce irradiation of adjacent quadrupoles

## Slide 19: Estimated wire impact on luminosity
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Without crab cavities (CC), integrated luminosity (per day) is reduced by 13 %
Wires partially restore lost performance
In the presence of CC and wire a slight increase of integrated luminosity is guaranteed
Baseline
No CC
-13%
-6%
+3%
[fb-1]
No CC with Wire
With CC
and Wire
-5%
Round
Flat
Round
or Flat
Round
Round

## Slide 20: Outline
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Introduction
  terminology
Wire corrector
  concept
  first proof of concept
  numerical calculations
Wire corrector system (P530)
  components
  prototype
TRIUMF expertise
  beam dynamics
  engineering
Summary

## Slide 21: Main Design Features: Wire and Insulator
TRIUMF & ATLAS Canada seminar - September 21st , 2021
The present design for the prototype plans a 1 mm Mo wire with max. 150 A current
Mo wire has higher electrical resistivity compared to Cu (back-up), but is better matching ceramic temperature expansion (higher robustness)
The ceramics is AlN (Aluminum Nitride)
slots to reduce thermally induced stresses during brazing
AlN segmented ceramic insulator
Mo thin metal wire (Ø 1 mm)

## Slide 22: Low-cost modular design (proposal) from CERN
Insulator with wire is mechanically clamped to a Cu-based housing, via controlled-torque screws
Cu clamps to be designed to minimize RF impedance
Wire active length 1 m; several insulator modules to be assembled (250 ÷ 300 mm long)
TRIUMF & ATLAS Canada seminar - September 21st , 2021

## Slide 23: Vacuum chamber and feedthrough
Water cooling channel obtained by housing machining and cover welding. Cu half-shell welded to the housing.
Commercial feedthrough connection carrying up to 185 A. If more current is needed, liquid-cooled feedthroughs should be adopted
Stainless steel flange brazed to copper and then welded to vacuum chamber. TRIUMF proposes and accessible vacuum chamber!
TRIUMF & ATLAS Canada seminar - September 21st , 2021
weld
weld
weld
brazing
feedthrough

## Slide 24: Main assembly
B1
B2
Wire module
Beam position monitor
Automatic beam alignment
Bellow (RF module)
Frame and support
TRIUMF & ATLAS Canada seminar - September 21st , 2021
6 wire modules (wire in vacuum chamber) per assembly
4 assemblies: 2 (upstream and downstream) per IP (ATLAS and CMS)
Table from O. Kester document

## Slide 25: Proof of Concept - Demonstrator
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Vacuum brazing is the most critical step in the process (few mm gap between wire and cooler may induce a thermal runaway of hundreds degrees …)  proof of concept proposed
On this basis a low-cost short demonstrator (290 mm long) has been built and tested to validate the concept and perform online measurements
A series of optical viewports allows measuring wire and insulator temperatures (IR camera and/or pyrometer) and wire deflection while varying current

## Slide 26: Demonstrator prototype
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Components of the demonstrator procured
2 wire diameters (Ø0.8 and Ø1 mm) successfully brazed on AlN housings at CERN main workshop
Good adhesion throughout the length, only minor braze lacks at the ends
Thermo-physically characterization of AlN to ascertain its properties as a function of temperature
1 mm

## Slide 27: Demonstrator prototype – vacuum chamber
TRIUMF & ATLAS Canada seminar - September 21st , 2021

## Slide 28: Prototype testing outcome
TRIUMF & ATLAS Canada seminar - September 21st , 2021
A simple, low-cost, modular design is being explored, allowing a certain scalability as to number of modules, current and dimensions
No showstoppers identified for thin Mo naked wire (Ø ≥ 0.8 mm) brazed onto a ceramic insulator
However, preliminary investigations ignored several key physical and technological aspects (e.g. beam and RF losses, mechanical feasibility, fabrication tolerances, UHV aspects etc.) which should be the object of a proper design study
The manufacturing of a demonstrator is a fundamental step to validate the concept. A simplified demo is foreseen by Autumn 2021. Tests expected to follow in Winter 21/22
A full-fledged design (number of modules, length, interfaces, motorization, integration…) should be launched after demonstrator proves this concept is viable.

## Slide 29: Outline
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Introduction
  terminology
Wire corrector
  concept
  first proof of concept
  numerical calculations
Wire corrector system (P530)
  components
  prototype
TRIUMF expertise
  beam dynamics
  engineering
Summary

## Slide 30: A call for TRIUMF and the Canadian scientific community
TRIUMF & ATLAS Canada seminar - September 21st , 2021

## Slide 31: Beam dynamics group
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Canada contributes via TRIUMF beam physics support including the wire compensation activities in the LHC;
Dobrin works on wire optimization with H driving terms – extension into 2D. Short-term tracking test with MadX and the BB Invariant
Testing wire on sixtrack (long term track and DA tune-scans) Support for Yannis, Kyriacos and Nikos who are running DA calculations with wire
In the long term: moving to flat-beam optics scenario for both of the above points

## Slide 32: Engineering physics group
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Beam optics design (in collaboration with beam dynamics group)
Electrostatic (RIB transport) and magnetic (HRS) elements design
  OPERA® electro-magnetic field calculations
Hardware design, engineering and installation (including alignment) of electrostatic and magnetic beamlines
UHV cleaning and assembly procedure
ARIEL RIB transport system: 200+ m of electrostatic beamlines
High Resolution Separator
HRS multipole

## Slide 33: TRIUMF available expertise
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Controls
Power converters (high current and high voltage)
Vacuum
Diagnostics (provided BPM for CERN awake)
Radio Frequency (providing crab cavity cryomodules)
Alignment (laser tracker)
Design and manufacturing
TRIUMF e-linac BPM
TRIUMF Twin Quadrupole Magnet for the LHC

## Slide 34: Outline
TRIUMF & ATLAS Canada seminar - September 21st , 2021
Introduction
  terminology
Wire corrector
  concept
  first proof of concept
  numerical calculations
Wire corrector system (P530)
  components
  prototype
TRIUMF expertise
  beam dynamics
  engineering
Summary

## Slide 35: Summary
TRIUMF & ATLAS Canada seminar - September 21st , 2021
The non-linear part of the BBLR interactions appears to be the dominant mechanism for beam blow-up and beam losses, hence reduce integrated luminosity
Wire correctors are a simple way to compensate for BBLR non-linearity and therefore reduce beam losses
Initial experiments carried out with a non-optimum apparatus (wire-in-collimator) already demonstrated the viability of this solution
Initial calculations also point in the same direction of increased integrated luminosity
Initial prototype of the improved hardware configuration has been tested at CERN
CERN called for TRIUMF and the Canadian scientific community support to build the wire corrector system
TRIUMF has the in-house capabilities for supporting CERN and contributing to the design and manufacturing of the final optimized wire compensation system

## Slide 36: Thank you Merci
Follow us @TRIUMFLab
www.triumf.ca
HL-LHC Wire Compensation Meeting, FERMILAB, 17th October 2019