## Slide 1
The User Facility Radiation Source ELBE @ HZDR
Peter Michel
e-Linac Reliability Workshop (ERW), May 9-10, 2022, virtual
HZDR
ELBE facility
Management and user aspects
Accelerator R&D @ ELBE

## Slide 2
Dresden
ELBE Center for High Power Radiation Sources
Electron Linear accelerator with high Brilliance and low Emittance
HELMHOLTZ ZENTRUM DRESDEN-ROSSENDORF (HZDR)
Helmholtz-Zentrum Dresden-Rossendorf
member of the Helmholtz Association since 2011
~ 1,100 . employees incl. ~ 350 scientists + 150 PHD
research Sites : DRESDEN, Leipzig, Freiberg, Schenefeld near Hamburg, Grenoble (FR)

## Slide 3
nano scale systems
ultra fast dynamics of solids
i.p.correlated syst., low dimensional syst.
(future: soft matter…biol. samples)
nuclear structure (nuclear & astro physics)
defect analysis (material research)
nuclear data (nucl. science & technology)
detector technology
radio biology
detector technology
radiation hardness studies
Terahertz and Infrared
Bremsstrahlung
Positrons
Neutrons
Electrons
ELBE Electron Accelerator
ELBE concept

## Slide 4
ELBE Layout
coherent IR-radiation 5 – 250 µm
THz radiation
100 µm – 3 mm
electrons
30 – 34MeV
Bremsstrahlung
0 – 17 MeV
pulsed, mono-energetic
positrons 0.2 – 30 keV
electron laser interaction
~ 100 M€ investment
~ 50 FTE
~ 8 M€/y operating cost
1mA, 40MeV CW electron accelerator

## Slide 5
ELBE Electron Accelerator
1.3 GHz sc linac
18 MeV
250 kV DC gun
77 pC
10 mm mrad
3 MeV SRF photo gun
~ 200 pC 1 nC
3 mm mrad
RF bunch
compressor
magnetic bunch
compressor
1.3 GHz sc linac
18 MeV
CW
100µs – 36ms
0 – 1s
macro pulse
26 MHz – kHz
single pulse
1-10 ps
250fs
1 - 231 bunches

## Slide 6
ELBE CW-Linac Module
250 keV, 1 mA
9-cell Tesla Cavity
1,3 GHz
2 K Helium vessel
Helium Liquifier LINDE
200 W @ 1.8 K
Tuning System
Isolation Vacuum / LN2-Shield
2x10kW SSA
Bruker
18 MeV, 1 mA
4 GLS /Daresbury UK
TARLA /Turkey
MESA/Uni Mainz Germany
POLFEL/Poland
License Agreement on the Twin Cavity Module with HZDR/Rossendorf

## Slide 7
Technological challenges at ELBE
Superconducting gun + accelerator
High beam power
High demands on electron beam quality
low emittance
extremely short pulses < ps
high bunch charge
High precision beam diagnostics

## Slide 8
full CW accelerators
ELBE
SRF gun
thermionic gun
pulsed superconducting
accelerators
FLASH, XFEL
bunches / s
bunch charge / pC
1000
100
103
107
104
105
106
optical resonator FEL
high charge, adjustable pulse distance (>µs)
cTHz, nTOF, positrons
What is unique at the ELBE accelerator ?
normal conducting accelerators
FELIX, FLARE, CLIO, FHI…

## Slide 9
hours in total:
Scheduled 6736
Used 6426
Reliability 94%
External users: 70 %
reliability
Beam time statistics 2020/2021 (Run II/20-RunII/21 !)
Chart: 
| Extern | Intern
 | 0.76684 | 0.23316
Chart: Beamtime distribution 2020/21 R2-R2
| NP | RP | NEP | FEL | POS | IP | THz | MD
 | 0.10749 | 0.054737 | 0.082511 | 0.15271 | 0.12771 | 0.036803 | 0.15218 | 0.28586
External/Internal use (beamtime)
Chart: 
| 2007 | 2008 | 2008/9 | 2009/10 | 2010/11 | 2011/12 | 2012/13 | 2013/14 | 2014/15 | 2015/16 | 2016/17 | 2017/18 | 2018/19 | 2019/20 | 2020/21
 | 0.76233 | 0.89283 | 0.86459 | 0.8053 | 0.87027 | 0.89415 | 0.92 | 0.914 | 0.881 | 0.82 | 0.85 | 0.94 | 0.95 | 0.95 | 0.94

## Slide 10
Beam time management at ELBE
Call for proposals twice per year
Beamline scientist evaluate for feasibility of proposed experiments
Proposal evaluation by ELBE SAC (provides ranking , over booking factor 2…3)
Beam time allocated for a six month block of shifts
Beamline scientists support users
Proposal application/evaluation/reporting through GATE portal (internet)

## Slide 11
First Beam
May 21st 2001
6MeV 5µA
2001
Comm.
& test
operation
2004
2 shift
user
operation
ELBE
Follow up
DALI
?
~ 20 years with cavities at 2 K
~ 120.000 hours operation
> 100 kC accelerated charge
ELBE Timeline
2022
SRF Gun operation
Since 2016
24/7 user operation
2008
THz-Upgrade
2010-14

## Slide 12
Overall concept for THz/IR source DALI
P. Evtushenko et al., FEL 2019 Conference

## Slide 13
Accelerator Research and Development @ HZDR
Controlled injection at high
peak current electron beam
Single-shot ultrafast probing of
plasma waves and beam
characterization
Advanced radiation sources
Plasma target development
Computing & simulations
SRF gun cavity optimization
gun cryostat development
photo cathodes for SRF guns
long term studies
THz based e-beam diagnostic
Advanced beam diagnostics for short pulse & high power cw beams
Synchronization , stabilization & feed-back , digital LL RF control
Sc RF photo injectors for CW
Ultra short beams, diagnostic & control
Laser Particle acceleration

## Slide 14
Thank you for your attention